## Slide 1: Distance vector algorithm
Bellman-Ford equation (dynamic programming)
let
dx(y) := cost of least-cost path from x to y
then
dx(y) = min {c(x,v) + dv(y) }
v
cost to neighbor v
min taken over all neighbors v of x
cost from neighbor v to destination y

## Slide 2: Distance vector algorithm
Dx(y) = estimate of least cost from x to y
  x maintains distance vector Dx = [Dx(y): y є N ]
node x:
  knows cost to each neighbor v: c(x,v)
  Receives and maintains its neighbors’ distance vectors. For each neighbor v, x maintains Dv = [Dv(y): y є N ]

## Slide 3: Distance vector algorithm
key idea:
from time-to-time, each node sends its own distance vector estimate to neighbors
when x receives new DV estimate from neighbor v, it updates its own DV using B-F equation:
Dx(y) ← minv{c(x,v) + Dv(y)} for each node y ∊ N
under minor, natural conditions, the estimate Dx(y) converge to the actual least cost dx(y)

## Slide 4: Distance vector algorithm
iterative, asynchronous: each local iteration caused by:
local link cost change
DV update message from neighbor
distributed:
each node notifies neighbors only when its DV changes
  neighbors then notify their neighbors if necessary
wait for (change in local link cost or msg from neighbor)
recompute estimates
if DV to any dest has changed, notify neighbors
each node:

## Slide 5: Distance-Vector (DV) Algorithm
At each node, x:
Initialization:
for all destinations y in N: Dx(y) = c(x,y) /* if y is not a neighbor then c(x,y) = ∞ */
for each neighbor w Dw(y) = ? (∞ )for all destinations y in N
for each neighbor w send distance vector Dx = [Dx(y): y in N] to w

## Slide 6: Distance-Vector (DV) Algorithm (contd.)
loop wait (until I see a link cost change to some neighbor w or until I receive a distance vector from some neighbor v)
for each y in N: Dx(y) = minv{c(x,v) + Dv(y)}
if Dx(y) changed for any destination y send distance vector Dx = [Dx(y): y in N] to all neighbors
forever

## Slide 7: Example - initial distances
A
B
E
C
D
Info at
node
A
B
C
D
A
B
C
0
7
~
7
0
1
~
1
0
~
~
2
7
1
1
2
2
8
Distance to node
D
~
~
2
0
E
1
8
~
2
1
8
~
2
0
E

## Slide 8: E receives D’s routes
A
B
E
C
D
Info at
node
A
B
C
D
A
B
C
0
7
~
7
0
1
~
1
0
~
~
2
7
1
1
2
2
8
Distance to node
D
~
~
2
0
E
1
8
~
2
1
8
~
2
0
E

## Slide 9: E updates cost to C
A
B
E
C
D
Info at
node
A
B
C
D
A
B
C
0
7
~
7
0
1
~
1
0
~
~
2
7
1
1
2
2
8
Distance to node
D
~
~
2
0
E
1
8
4
2
1
8
~
2
0
E

## Slide 10: A receives B’s routes
A
B
E
C
D
Info at
node
A
B
C
D
A
B
C
0
7
~
7
0
1
~
1
0
~
~
2
7
1
1
2
2
8
Distance to node
D
~
~
2
0
E
1
8
4
2
1
8
~
2
0
E

## Slide 11: A updates cost to C
A
B
E
C
D
Info at
node
A
B
C
D
A
B
C
0
7
8
7
0
1
~
1
0
~
~
2
7
1
1
2
2
8
Distance to node
D
~
~
2
0
E
1
8
4
2
1
8
~
2
0
E

## Slide 12: A receives E’s routes
A
B
E
C
D
Info at
node
A
B
C
D
A
B
C
0
7
8
7
0
1
~
1
0
~
~
2
7
1
1
2
2
8
Distance to node
D
~
~
2
0
E
1
8
4
2
1
8
~
2
0
E

## Slide 13: A updates cost to C and D
A
B
E
C
D
Info at
node
A
B
C
D
A
B
C
0
7
5
7
0
1
~
1
0
~
~
2
7
1
1
2
2
8
Distance to node
D
3
~
2
0
E
1
8
4
2
1
8
~
2
0
E

## Slide 14: Final distances
A
B
C
D
Info at
node
A
B
C
D
A
B
C
0
6
5
6
0
1
5
1
0
3
3
2
7
1
1
2
2
8
Distance to node
D
3
3
2
0
E
1
5
4
2
1
5
4
2
0
E
E

## Slide 15: View from a node
A
B
E
C
D
dest
A
B
C
D
A
B
D
1
14
5
7
8
5
6
9
4
4
11
2
7
1
1
2
2
8
Next hop
E’s routing table
Actually only the lowest cost to the destination matters.
A ➜ next hop is A, with cost 1
B ➜ next hop is D, with cost 5

## Slide 16: Distance vector: link cost changes
link cost changes:
node detects local link cost change
updates routing info, recalculates distance vector
if DV changes, notify neighbors
“good
news
travels
fast”
x
z
1
4
50
y
1
t0 : y detects link-cost change, updates its DV, informs its neighbors.
t1 : z receives update from y, updates its table, computes new least cost to x , sends its neighbors its DV.
t2 : y receives z’s update, updates its distance table. y’s least costs do not change, so y does not send a message to z.

## Slide 17: Distance vector: link cost changes
link cost changes:
node detects local link cost change
bad news travels slow - “count to infinity” problem!
44 iterations before algorithm stabilizes: see text
x
z
1
4
50
y
60
poisoned reverse:
If Z routes through Y to get to X :
  Z tells Y its (Z’s) distance to X is infinite (so Y won’t route to X via Z)
will this completely solve count to infinity problem?

## Slide 18: Slow Convergence with Link Cost Increase
Before change, t0 : Dy(x)=4, Dy(z)=1, Dz(y)=1, Dz(x)=5
y detects cost change from 4 to 60. Computes new min. cost path to x:
Dy(x) = min {c(y,x)+Dx(x), c(y,z)+Dz(x)} =min{60+0,1+5}= 6
y only has local information – z had last indicated that z could reach x with a cost of 5. So, that is used, even though ‘we’ know z really was coming back through y. Let z detect cost change to x from 5 to 50.
Creates a Routing Loop
After z receives y’s new distance vector(min. cost to x=6) it will compute: Dz(x) = min {50+0, 1+6} = 7. Informs y
y now recomputes
Dy(x) = min {c(y,x)+Dx(x), c(y,z)+Dz(x)} =min{60+0,1+7}= 8
x
z
1
4
5
y
60
50

## Slide 19: Slow Convergence with Link Cost Increase
After z receives y’s new distance vector(min. cost to x=8) it will compute: Dz(x) = min {50+0, 1+8} = 9. Informs y
This will continue until z finally gets to have a cost going through y is greater than 50. Then, it will determine least cost path is directly to x at a cost of 50
44 iterations.
If the link cost from y to x changed to 10,000, and c(z,x) = 9999, then it would take 9995 iterations.
Hence called ‘count to infinity’ problem.
Main issue: Loop persists during this time!
x
z
1
4
5
y
60
50

## Slide 20: Adding Poisoned Reverse
If z routes through y to get to destination x, then z will advertise to y that its distance to x is infinity. That is, z will advertise to y that Dz(x) = ∞
So, y believes that z has no path to x through z.
So, when cost of (x,y) changes from 4 to 60, y updates table and continues to route directly to x, even with the higher cost of 60.
Informs z of new cost Dy(x) = 60
z shifts to direct link (z,x), and informs y that Dz(x) = 50
y updates its distance table; so Dy(x) = 51 and z is on the least cost path to x
Then, y poisons reverse path from z to x; tells z that Dy(x) = ∞
x
z
1
4
50
y
60

## Slide 21: Hierarchical routing
aggregate routers into regions, “autonomous systems” (AS)
routers in same AS run same routing protocol
  “intra-AS” routing protocol
  routers in different AS can run different intra-AS routing protocols
gateway router:
at “edge” of its own AS
has link to router in another AS
Run inter-AS routing protocols between ASs

## Slide 22: Interconnected ASes
3b
1d
3a
1c
2a
AS3
AS1
AS2
1a
2c
2b
1b
Intra-AS
Routing
algorithm
Inter-AS
Routing
algorithm
Forwarding
table
3c
forwarding table configured by both intra- and inter-AS routing algorithm
  intra-AS sets entries for internal dests
  inter-AS & intra-AS sets entries for external dests

## Slide 23: Inter-AS tasks
suppose router in AS1 receives datagram destined outside of AS1:
  router should forward packet to gateway router, but which one?
AS1 must:
learn which dests are reachable through AS2, which through AS3
propagate this reachability info to all routers in AS1
job of inter-AS routing!
AS3
AS2
3b
3c
3a
AS1
1c
1a
1d
1b
2a
2c
2b
other
networks
other
networks

## Slide 24: Example: setting forwarding table in router 1d
suppose AS1 learns (via inter-AS protocol) that subnet x reachable via AS3 (gateway 1c), but not via AS2
  inter-AS protocol propagates reachability info to all internal routers
router 1d determines from intra-AS routing info that its interface I is on the least cost path to 1c
  installs forwarding table entry (x,I)
AS3
AS2
3b
3c
3a
AS1
1c
1a
1d
1b
2a
2c
2b
other
networks
other
networks
x
…

## Slide 25: Example: choosing among multiple ASes
now suppose AS1 learns from inter-AS protocol that subnet x is reachable from AS3 and from AS2.
to configure forwarding table, router 1d must determine which gateway it should forward packets towards, for dest x
  this is also job of inter-AS routing protocol!
AS3
AS2
3b
3c
3a
AS1
1c
1a
1d
1b
2a
2c
2b
other
networks
other
networks
x
……
…
?

## Slide 26: Hierarchical OSPF
boundary router
backbone router
area 1
area 2
area 3
backbone
area
border
routers
internal
routers

## Slide 27: Hierarchical OSPF
two-level hierarchy: local area, backbone.
  link-state advertisements only in area
  each nodes has detailed area topology; only know direction (shortest path) to nets in other areas.
area border routers: “summarize” distances to nets in own area, advertise to other Area Border routers.
backbone routers: run OSPF routing limited to backbone.
boundary routers: connect to other AS’s.

## Slide 28: Internet inter-AS routing: BGP
BGP (Border Gateway Protocol): the de facto inter-domain routing protocol
  “glue that holds the Internet together”
BGP provides each AS a means to:
  eBGP: obtain subnet reachability information from neighboring ASs.
  iBGP: propagate reachability information to all AS-internal routers.
  determine “good” routes to other networks based on reachability information and policy.
allows subnet to advertise its existence to rest of Internet: “I am here”

## Slide 29: Internet inter-AS routing: BGP
BGP (Border Gateway Protocol)
Path Vector protocol:
  similar to Distance Vector protocol
  each Border Gateway broadcast to neighbors (peers) entire path (i.e., sequence of AS’s) to destination
  BGP routes to networks (ASs), not individual hosts
  E.g., Gateway X may send its path to dest. Z:
Path (X,Z) = X,Y1,Y2,Y3,…,Z

## Slide 30: Internet inter-AS routing: BGP
Suppose: gateway X send its path to peer gateway W
W may or may not select path offered by X
  cost, policy (don’t route via competitors AS), loop prevention reasons.
If W selects path advertised by X, then:
Path (W,Z) = w, Path (X,Z)
Note: X can control incoming traffic by controlling its route advertisements to peers:
  e.g., don’t want to route traffic to Z -> don’t advertise any routes to Z

## Slide 31: BGP Operations (Simplified)
Establish session on
TCP port 179
Exchange all
active routes
Exchange incremental
updates
AS1
AS2
While connection
is ALIVE exchange
route UPDATE messages
BGP session

## Slide 32: BGP basics
when AS3 advertises a prefix to AS1:
  AS3 promises it will forward datagrams towards that prefix
  AS3 can aggregate prefixes in its advertisement
AS3
AS2
3b
3c
3a
AS1
1c
1a
1d
1b
2a
2c
2b
other
networks
other
networks
BGP session: two BGP routers (“peers”) exchange BGP messages:
  advertising paths to different destination network prefixes (“path vector” protocol)
  exchanged over semi-permanent TCP connections
BGP
message

## Slide 33: BGP basics: distributing path information
AS3
AS2
3b
3a
AS1
1c
1d
1a
1b
2a
2c
2b
other
networks
other
networks
using eBGP session between 3a and 1c, AS3 sends prefix reachability info to AS1.
  1c can then use iBGP to distribute new prefix info to all routers in AS1
  1b can then re-advertise new reachability info to AS2 over 1b-to-2a eBGP session
when router learns of new prefix, it creates entry for that prefix in its forwarding table.
eBGP session
iBGP session

## Slide 34: Path attributes and BGP routes
advertised prefix includes BGP attributes
  prefix + attributes = “route”
two important attributes:
  AS-PATH: contains ASs through which prefix advertisement has passed: e.g., AS 67, AS 17
  NEXT-HOP: indicates specific internal-AS router to next-hop AS. (may be multiple links from current AS to next-hop-AS) - remember this is from the ‘advertiser’s end’
gateway router receiving route advertisement uses import policy to accept/decline
  e.g., never route through AS x
  policy-based routing

## Slide 35: BGP route selection
router may learn about more than 1 route to destination AS, selects route based on:
  local preference value attribute: policy decision
  shortest AS-PATH
  closest NEXT-HOP router: hot potato routing
  additional criteria
2a
2c
1a
1b
other
networks
other
networks

## Slide 36: Path Vectors
Each routing update carries the entire path
Loops are detected as follows:
  when AS gets a route, check if AS already in path
  if yes, reject route
  if no, add self and advertise route further
Advantage:
  metrics are local - AS chooses path, protocol ensures no loops

## Slide 37: BGP Example
Speaker for AS2 advertises reachability to P and Q
  network 128.96, 192.4.153, 192.4.32, and 192.4.3, can be reached directly from AS2
Speaker for backbone advertises
  networks 128.96, 192.4.153, 192.4.32, and 192.4.3 can be reached along the path (AS1, AS2).
Speaker can cancel previously advertised paths
Backbone network
(AS 1)
Regional provider A
(AS 2)
Regional provider B
(AS 3)
Customer P
(AS 4)
Customer Q
(AS 5)
Customer R
(AS 6)
Customer S
(AS 7)
128.96
192.4.153
192.4.32
192.4.3
192.12.69
192.4.54
192.4.23

## Slide 38: Shorter Doesn’t Always Mean Shorter
AS 4
AS 3
AS 2
AS 1
BGP says that
path 4 1 is better
than path 3 2 1
??
In fairness:
could you do
this “right” and
still scale?
Exporting internal
state would
dramatically
increase global
instability and
amount of routing
state

## Slide 39
High-level overview
Router becomes aware of prefix
Router determines output port for prefix
Router enters prefix-port in forwarding table
How does entry get in forwarding table?

## Slide 40: Router becomes aware of prefix
AS3
AS2
3b
3c
3a
AS1
1c
1a
1d
1b
2a
2c
2b
other
networks
other
networks
BGP
message
BGP message contains “routes”
“route” is a prefix and attributes: AS-PATH, NEXT-HOP,…
Example: route:
  Prefix:138.16.64/22 ; AS-PATH: AS3 AS131 ; NEXT-HOP: 201.44.13.125

## Slide 41: Router may receive multiple routes
AS3
AS2
3b
3c
3a
AS1
1c
1a
1d
1b
2a
2c
2b
other
networks
other
networks
BGP
message
Router may receive multiple routes for same prefix
Has to select one route

## Slide 42: Select best BGP route to prefix
Router selects route based on shortest AS-PATH
Example:
  AS2 AS17 to 138.16.64/22
  AS3 AS131 AS201 to 138.16.64/22
What if there is a tie? We’ll come back to that!
select

## Slide 43: Find best intra-route to BGP route
Use selected route’s NEXT-HOP attribute
  Route’s NEXT-HOP attribute is the IP address of the router interface that begins the AS PATH.
Example:
  AS-PATH: AS2 AS17 ; NEXT-HOP: 111.99.86.55
Router uses OSPF to find shortest path from 1c to 111.99.86.55
AS3
AS2
3b
3c
3a
AS1
1c
1a
1d
1b
2a
2c
2b
other
networks
other
networks
111.99.86.55

## Slide 44: Router identifies port for route
Identifies port along the OSPF shortest path
Adds prefix-port entry to its forwarding table:
  (138.16.64/22 , port 4)
AS3
AS2
3b
3c
3a
AS1
1c
1a
1d
1b
2a
2c
2b
other
networks
other
networks
router port
1
2
3
4

## Slide 45: Hot Potato Routing
Suppose there two or more best inter-AS routes.
Then choose route with closest NEXT-HOP
  Use OSPF to determine which gateway is closest
  Q: From 1c, chose AS3 AS201 or AS2 AS17?
  A: route AS3 AS201 since it is closer
AS3
AS2
3b
3c
3a
AS1
1c
1a
1d
1b
2a
2c
2b
other
networks
other
networks

## Slide 46: How does entry get in forwarding table?
Summary
Router becomes aware of prefix
  via BGP route advertisements from other routers
Determine router output port for prefix
  Use BGP route selection to find best inter-AS route
  Use OSPF to find best intra-AS route leading to best inter-AS route
  Router identifies router port for that best route
Enter prefix-port entry in forwarding table

## Slide 47: BGP routing policy
A,B,C are provider networks
X,W,Y are customer (of provider) networks
X is dual-homed: attached to two networks
  X does not want to route from B via X to C
  .. so X will not advertise to B a route to C
A
B
C
W
X
Y
legend:
customer
network:
provider
network

## Slide 48: BGP routing policy (2)
A advertises path AW to B
B advertises path BAW to X
Should B advertise path BAW to C?
  No way! B gets no “revenue” for routing CBAW since neither W nor C are B’s customers
  B wants to force C to route to w via A
  B wants to route only to/from its customers!
A
B
C
W
X
Y
legend:
customer
network:
provider
network

## Slide 49: Link layer services
framing, link access:
  encapsulate datagram into frame, adding header, trailer
  channel access if shared medium
  “MAC” addresses used in frame headers to identify source, dest
    different from IP address!
reliable delivery between adjacent nodes
  we learned how to do this already (chapter 3)!
  seldom used on low bit-error link (fiber, some twisted pair)
  wireless links: high error rates
    Q: why both link-level and end-end reliability?

## Slide 50: Link layer services (more)
flow control:
  pacing between adjacent sending and receiving nodes
error detection:
  errors caused by signal attenuation, noise.
  receiver detects presence of errors:
    signals sender for retransmission or drops frame
error correction:
  receiver identifies and corrects bit error(s) without resorting to retransmission
half-duplex and full-duplex
  with half duplex, nodes at both ends of link can transmit, but not at same time

## Slide 51: MAC addresses and ARP
32-bit IP address:
  network-layer address for interface
  used for layer 3 (network layer) forwarding
MAC (or LAN or physical or Ethernet) address:
  function: used ‘locally” to get frame from one interface to another physically-connected interface (same network, in IP-addressing sense)
  48 bit MAC address (for most LANs) burned in NIC ROM, also sometimes software settable
  e.g.: 1A-2F-BB-76-09-AD
hexadecimal (base 16) notation
(each “number” represents 4 bits)

## Slide 52: LAN addresses and ARP
each adapter on LAN has unique LAN address
adapter
1A-2F-BB-76-09-AD
58-23-D7-FA-20-B0
0C-C4-11-6F-E3-98
71-65-F7-2B-08-53
LAN
(wired or
wireless)

## Slide 53: LAN addresses (more)
MAC address allocation administered by IEEE
manufacturer buys portion of MAC address space (to assure uniqueness)
analogy:
  MAC address: like Social Security Number
  IP address: like postal address
MAC flat address ➜ portability
  can move LAN card from one LAN to another
IP hierarchical address not portable
  address depends on IP subnet to which node is attached

## Slide 54: ARP: address resolution protocol
ARP table: each IP node (host, router) on LAN has table
  IP/MAC address mappings for some LAN nodes:
< IP address; MAC address; TTL>
  TTL (Time To Live): time after which address mapping will be forgotten (typically 20 min)
Question: how to determine
interface’s MAC address, knowing its IP address?
1A-2F-BB-76-09-AD
58-23-D7-FA-20-B0
0C-C4-11-6F-E3-98
71-65-F7-2B-08-53
LAN
137.196.7.23
137.196.7.78
137.196.7.14
137.196.7.88

## Slide 55: ARP protocol: same LAN
A wants to send datagram to B
  B’s MAC address not in A’s ARP table.
A broadcasts ARP query packet, containing B's IP address
  dest MAC address = FF-FF-FF-FF-FF-FF
  all nodes on LAN receive ARP query
B receives ARP packet, replies to A with its (B's) MAC address
  frame sent to A’s MAC address (unicast)
A caches (saves) IP-to-MAC address pair in its ARP table until information becomes old (times out)
  soft state: information that times out (goes away) unless refreshed
ARP is “plug-and-play”:
  nodes create their ARP tables without intervention from net administrator

## Slide 56: Addressing: routing to another LAN
walkthrough: send datagram from A to B via R
  focus on addressing – at IP (datagram) and MAC layer (frame)
  assume A knows B’s IP address
  assume A knows IP address of first hop router, R (how?)
  assume A knows R’s MAC address (how?)
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B

## Slide 57: Addressing: routing to another LAN
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
IP
Eth
Phy
IP src: 111.111.111.111
IP dest: 222.222.222.222
A creates IP datagram with IP source A, destination B
A creates link-layer frame with R's MAC address as dest, frame contains A-to-B IP datagram
MAC src: 74-29-9C-E8-FF-55
MAC dest: E6-E9-00-17-BB-4B

## Slide 58: Addressing: routing to another LAN
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
IP
Eth
Phy
frame sent from A to R
IP
Eth
Phy
frame received at R, datagram removed, passed up to IP
MAC src: 74-29-9C-E8-FF-55
MAC dest: E6-E9-00-17-BB-4B
IP src: 111.111.111.111
IP dest: 222.222.222.222
IP src: 111.111.111.111
IP dest: 222.222.222.222

## Slide 59: Addressing: routing to another LAN
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
IP src: 111.111.111.111
IP dest: 222.222.222.222
R forwards datagram with IP source A, destination B
R creates link-layer frame with B's MAC address as dest, frame contains A-to-B IP datagram
MAC src: 1A-23-F9-CD-06-9B
MAC dest: 49-BD-D2-C7-56-2A
IP
Eth
Phy
IP
Eth
Phy

## Slide 60: Addressing: routing to another LAN
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
R forwards datagram with IP source A, destination B
R creates link-layer frame with B's MAC address as dest, frame contains A-to-B IP datagram
IP src: 111.111.111.111
IP dest: 222.222.222.222
MAC src: 1A-23-F9-CD-06-9B
MAC dest: 49-BD-D2-C7-56-2A
IP
Eth
Phy
IP
Eth
Phy

## Slide 61: Addressing: routing to another LAN
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
R forwards datagram with IP source A, destination B
R creates link-layer frame with B's MAC address as dest, frame contains A-to-B IP datagram
IP src: 111.111.111.111
IP dest: 222.222.222.222
MAC src: 1A-23-F9-CD-06-9B
MAC dest: 49-BD-D2-C7-56-2A
IP
Eth
Phy

## Slide 62: Ethernet frame structure
sending adapter encapsulates IP datagram (or other network layer protocol packet) in Ethernet frame
preamble:
7 bytes with pattern 10101010 followed by one byte with pattern 10101011
used to synchronize receiver, sender clock rates
dest.
address
source
address
data (payload)
CRC
preamble
type

## Slide 63: Ethernet frame structure (more)
addresses: 6 byte source, destination MAC addresses
  if adapter receives frame with matching destination address, or with broadcast address (e.g. ARP packet), it passes data in frame to network layer protocol
  otherwise, adapter discards frame
type: 2 byte field indicates higher layer protocol (mostly IP but others possible, e.g., Novell IPX, AppleTalk)
CRC: cyclic redundancy check at receiver
  error detected: frame is dropped
dest.
address
source
address
data (payload)
CRC
preamble
type

## Slide 64: Ethernet: unreliable, connectionless
connectionless: no handshaking between sending and receiving NICs
unreliable: receiving NIC doesn’t send acks or nacks to sending NIC
  data in dropped frames recovered only if initial sender uses higher layer rdt (e.g., TCP), otherwise dropped data lost
Ethernet’s MAC protocol: unslotted CSMA/CD with binary exponential backoff

## Slide 65: Switch: multiple simultaneous transmissions
hosts have dedicated, direct connection to switch
switches buffer packets
Ethernet protocol used on each incoming link, but no collisions; full duplex
  each link is its own collision domain
switching: A-to-A’ and B-to-B’ can transmit simultaneously, without collisions
switch with six interfaces
(1,2,3,4,5,6)
A
A’
B
B’
C
C’
1
2
3
4
5
6

## Slide 66: Switch forwarding table
Q: how does switch know A’ reachable via interface 4, B’ reachable via interface 5?
switch with six interfaces
(1,2,3,4,5,6)
A
A’
B
B’
C
C’
1
2
3
4
5
6
A: each switch has a switch table, each entry:
  (MAC address of host, interface to reach host, time stamp)
  looks like a routing table!
Q: how are entries created, maintained in switch table?
  something like a routing protocol?

## Slide 67: Switch: self-learning
A
A’
B
B’
C
C’
1
2
3
4
5
6
switch learns which hosts can be reached through which interfaces
  when frame received, switch “learns” location of sender: incoming LAN segment
  records sender/location pair in switch table
A’ A
Dest: A’
Source: A
MAC addr interface TTL
Switch table
(initially empty)
A
1
60

## Slide 68: Switch: frame filtering/forwarding
when frame received at switch:
  1. record incoming link, MAC address of sending host
  2. index switch table using MAC destination address
  3. if entry found for destination then {
  if destination on segment from which frame arrived then drop frame
  else forward frame on interface indicated by entry
  }
  else flood /* forward on all interfaces except arriving
  interface */

## Slide 69: Self-learning, forwarding: example
A
A’
B
B’
C
C’
1
2
3
4
5
6
A’ A
Dest: A’
Source: A
MAC addr interface TTL
switch table
(initially empty)
A
1
60
A A’
A A’
A A’
A’ A
A’ A
frame destination, A’, location unknown:
flood
A A’
destination A location known:
A’
4
60
selectively send
on just one link

## Slide 70: Interconnecting switches
switches can be connected together
Q: sending from A to G - how does S1 know to forward frame destined to G via S4 and S3?
A: self learning! (works exactly the same as in single-switch case!)
A
B
S1
C
D
E
F
S2
S4
S3
H
I
G

## Slide 71: Self-learning multi-switch example
Suppose C sends frame to I, I responds to C
Q: show switch tables and packet forwarding in S1, S2, S3, S4
A
B
S1
C
D
E
F
S2
S4
S3
H
I
G

## Slide 72: VLANs
port-based VLAN: switch ports grouped (by switch management software) so that single physical switch ……
switch(es) supporting VLAN capabilities can be configured to define multiple virtual LANS over single physical LAN infrastructure.
Virtual Local
Area Network
1
8
9
16
10
2
7
…
Electrical Engineering
(VLAN ports 1-8)
Computer Science
(VLAN ports 9-16)
15
…
Electrical Engineering
(VLAN ports 1-8)
…
1
8
2
7
9
16
10
15
…
Computer Science
(VLAN ports 9-16)
… operates as multiple virtual switches

## Slide 73: Port-based VLAN
1
8
9
16
10
2
7
…
Electrical Engineering
(VLAN ports 1-8)
Computer Science
(VLAN ports 9-15)
15
…
traffic isolation: frames to/from ports 1-8 can only reach ports 1-8
  can also define VLAN based on MAC addresses of endpoints, rather than switch port
dynamic membership: ports can be dynamically assigned among VLANs
router
forwarding between VLANS: done via routing (just as with separate switches)
  in practice vendors sell combined switches plus routers

## Slide 74: VLANS spanning multiple switches
trunk port: carries frames between VLANS defined over multiple physical switches
  frames forwarded within VLAN between switches can’t be vanilla 802.1 frames (must carry VLAN ID info)
  802.1q protocol adds/removed additional header fields for frames forwarded between trunk ports
1
8
9
10
2
7
…
Electrical Engineering
(VLAN ports 1-8)
Computer Science
(VLAN ports 9-15)
15
…
2
7
3
Ports 2,3,5 belong to EE VLAN
Ports 4,6,7,8 belong to CS VLAN
5
4
6
8
16
1

## Slide 75
type
2-byte Tag Protocol Identifier
(value: 81-00)
Tag Control Information (12 bit VLAN ID field,
3 bit priority field like IP TOS)
Recomputed
CRC
802.1Q VLAN frame format
802.1 frame
802.1q frame
dest.
address
source
address
data (payload)
CRC
preamble
dest.
address
source
address
preamble
data (payload)
CRC
type

## Slide 76
Server racks
TOR switches
Tier-1 switches
Tier-2 switches
Load
balancer
Load
balancer
B
1
2
3
4
5
6
7
8
A
C
Border router
Access router
Data center networks
load balancer: application-layer routing
receives external client requests
directs workload within data center
returns results to external client (hiding data center internals from client)
Internet

## Slide 77
Server racks
TOR switches
Tier-1 switches
Tier-2 switches
1
2
3
4
5
6
7
8
Data center networks
rich interconnection among switches, racks:
  increased throughput between racks (multiple routing paths possible)
  increased reliability via redundancy

## Slide 78: Networking Objectives
Uniform high capacity
  Capacity between servers limited only by their NICs
  No need to consider topology when adding servers
    => In other words, high capacity between any two servers no matter which racks they are located in!
Performance isolation
  Traffic of one service should be unaffected by others
Ease of management: “Plug-&-Play” (layer-2 semantics)
  Flat addressing, so any server can have any IP address
  Server configuration is the same as in a LAN
  Legacy applications depending on broadcast must work

## Slide 79: A Scalable, Commodity Data Center Network Architecture
Main Goal: addressing the limitations of today’s data center network architecture
  single point of failure
  Over-subscription of links higher up in the topology
Key Design Considerations/Goals
  Allows host communication at line speed
    no matter where they are located!
  Backwards compatible with existing infrastructure
    no changes in application & support of layer 2 (Ethernet)
  Cost effective
    cheap infrastructure
    and low power consumption & heat emission

## Slide 80
Server racks
TOR switches
Tier-1 switches
Tier-2 switches
1
2
3
4
5
6
7
8
Data center networks: Fat Tree
rich interconnection among switches, racks:
  increased throughput between racks (multiple routing paths possible)
  increased reliability via redundancy
  The idea is that the edges at level k should have two or more times the capacity of the edges at level k+1 (the root is at level 0)

## Slide 81: Fat-Tree Based Topology (Cont.)
Why Fat-Tree?
  Fat tree has identical bandwidth at any bisection
    Bisection bandwidth: bandwidth across smallest cut that divides network into two equal halves
    Bandwidth across “narrowest” part of the network
  Each layer has the same aggregated bandwidth
Can be built using cheap devices with uniform capacity
  Each port supports same speed as end host
  All devices can transmit at line speed if packets are distributed uniformly along available paths
Great scalability
  k-port switch supports k3/4 servers

## Slide 82: Bisection Bandwith in a Fat Tree

## Slide 83
Software defined networking (SDN)
data
plane
control
plane
Remote Controller
CA
CA
CA
CA
CA
1: generalized“ flow-based” forwarding (e.g., OpenFlow)
2. control, data plane separation
3. control plane functions external to data-plane switches
…
4. programmable control applications
routing
access control
load
balance

## Slide 84
SDN perspective: data plane switches
Data plane switches
fast, simple, commodity switches implementing generalized data-plane forwarding (Section 4.4) in hardware
switch flow table computed, installed by controller
API for table-based switch control (e.g., OpenFlow)
  defines what is controllable and what is not
protocol for communicating with controller (e.g., OpenFlow)
data
plane
control
plane
SDN Controller
(network operating system)
…
routing
access
control
load
balance
southbound API
northbound API
SDN-controlled switches
network-control applications

## Slide 85
SDN perspective: SDN controller
SDN controller (network OS):
maintain network state information
interacts with network control applications “above” via northbound API
interacts with network switches “below” via southbound API
implemented as distributed system for performance, scalability, fault-tolerance, robustness
data
plane
control
plane
SDN Controller
(network operating system)
…
routing
access
control
load
balance
southbound API
northbound API
SDN-controlled switches
network-control applications

## Slide 86
SDN perspective: control applications
network-control apps:
“brains” of control: implement control functions using lower-level services, API provided by SDN controller
unbundled: can be provided by 3rd party: distinct from routing vendor, or SDN controller
data
plane
control
plane
SDN Controller
(network operating system)
…
routing
access
control
load
balance
southbound API
northbound API
SDN-controlled switches
network-control applications

## Slide 87
Network-wide distributed, robust state management
Communication to/from controlled devices
Link-state info
switch info
host info
statistics
flow tables
…
…
OpenFlow
SNMP
…
network graph
intent
RESTful
API
…
Interface, abstractions for network control apps
SDN
controller
routing
access
control
load
balance
Components of SDN controller
communication layer: communicate between SDN controller and controlled switches
Network-wide state management layer: state of network’s links, switches, services: a distributed database
Interface layer to network control apps: abstractions API

## Slide 88
SDN perspective: data plane switches
Data plane switches
fast, simple, commodity switches implementing generalized data-plane forwarding (Section 4.4) in hardware
switch flow table computed, installed by controller
API for table-based switch control (e.g., OpenFlow)
  defines what is controllable and what is not
protocol for communicating with controller (e.g., OpenFlow)
data
plane
control
plane
SDN Controller
(network operating system)
…
routing
access
control
load
balance
southbound API
northbound API
SDN-controlled switches
network-control applications

## Slide 89
SDN perspective: SDN controller
SDN controller (network OS):
maintain network state information
interacts with network control applications “above” via northbound API
interacts with network switches “below” via southbound API
implemented as distributed system for performance, scalability, fault-tolerance, robustness
data
plane
control
plane
SDN Controller
(network operating system)
…
routing
access
control
load
balance
southbound API
northbound API
SDN-controlled switches
network-control applications

## Slide 90
SDN perspective: control applications
network-control apps:
“brains” of control: implement control functions using lower-level services, API provided by SDN controller
unbundled: can be provided by 3rd party: distinct from routing vendor, or SDN controller
data
plane
control
plane
SDN Controller
(network operating system)
…
routing
access
control
load
balance
southbound API
northbound API
SDN-controlled switches
network-control applications

## Slide 91
Network-wide distributed, robust state management
Communication to/from controlled devices
Link-state info
switch info
host info
statistics
flow tables
…
…
OpenFlow
SNMP
…
network graph
intent
RESTful
API
…
Interface, abstractions for network control apps
SDN
controller
routing
access
control
load
balance
Components of SDN controller
communication layer: communicate between SDN controller and controlled switches
Network-wide state management layer: state of network’s links, switches, services: a distributed database
Interface layer to network control apps: abstractions API

## Slide 92: OpenFlow protocol
operates between controller, switch
TCP used to exchange messages
  optional encryption
three classes of OpenFlow messages:
  controller-to-switch
  asynchronous (switch to controller)
  symmetric (misc)
OpenFlow Controller

## Slide 93: OpenFlow: controller-to-switch messages
Key controller-to-switch messages
features: controller queries switch features, switch replies
configure: controller queries/sets switch configuration parameters
modify-state: add, delete, modify flow entries in the OpenFlow tables
packet-out: controller can send this packet out of specific switch port
OpenFlow Controller

## Slide 94: OpenFlow: switch-to-controller messages
Key switch-to-controller messages
packet-in: transfer packet (and its control) to controller. See packet-out message from controller
flow-removed: flow table entry deleted at switch
port status: inform controller of a change on a port.
Fortunately, network operators don’t “program” switches by creating/sending OpenFlow messages directly. Instead use higher-level abstraction at controller
OpenFlow Controller

## Slide 95: OpenFlow data plane abstraction
flow: defined by header fields
generalized forwarding: simple packet-handling rules
  Pattern: match values in packet header fields
  Actions: for matched packet: drop, forward, modify, matched packet or send matched packet to controller
  Priority: disambiguate overlapping patterns
  Counters: #bytes and #packets
Flow table in a router (computed and distributed by controller) define router’s match+action rules

## Slide 96: OpenFlow data plane abstraction
flow: defined by header fields
generalized forwarding: simple packet-handling rules
  Pattern: match values in packet header fields
  Actions: for matched packet: drop, forward, modify, matched packet or send matched packet to controller
  Priority: disambiguate overlapping patterns
  Counters: #bytes and #packets
src=1.2.*.*, dest=3.4.5.*  drop
src = *.*.*.*, dest=3.4.*.*  forward(2)
3. src=10.1.2.3, dest=*.*.*.*  send to controller
* : wildcard

## Slide 97: OpenFlow: Flow Table Entries
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Rule
Action
Stats
Forward packet to port(s)
Encapsulate and forward to controller
Drop packet
Send to normal processing pipeline
Modify Fields
Packet + byte counters
Link layer
Network layer
Transport layer
Notes: Now I’ll describe the API that tries to meet these goals.
97

## Slide 98
Destination-based forwarding:
*
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Action
*
*
*
*
*
51.6.0.8
*
*
*
port6
Examples
IP datagrams destined to IP address 51.6.0.8 should be forwarded to router output port 6
*
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Forward
*
*
*
*
*
*
*
*
22
drop
Firewall:
do not forward (block) all datagrams destined to TCP port 22
*
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Forward
*
*
*
*
128.119.1.1
*
*
*
*
drop
do not forward (block) all datagrams sent by host 128.119.1.1

## Slide 99
Destination-based layer 2 (switch) forwarding:
*
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Action
*
*
*
*
*
*
*
*
port3
Examples
layer 2 frames from MAC address 22:A7:23:11:E1:02 should be forwarded to output port 3
22:A7:23:
11:E1:02